## Slide 1
GREENWELD Impact Measurement - Part A

## Slide 2: Agenda
Key Green Welding Parameters
Measurement Types and Techniques for Green Welding
International Standard, European Legislation and Acceptance criteria
The influence of novel approaches on overall emission for environmentally friendly welding
Case Studies

## Slide 3: Key Green Welding Parameters
Fumes and Particulate Matter:
Metal Fumes: manganese, chromium, nickel, and other alloying elements
Particulate Matter (PM): Fine particulates can be released into the air during welding, contributing to air pollution.
Gases: Ozone, Nitrogen Oxides (NOx)
Volatile Organic Compounds (VOCs): Hydrocarbons
Oxides of Sulfur (SOx)
Welding Shielding Gases: Fluorinated Gases
Carbon Dioxide (CO2)
Emissions: Welding processes can generate various harmful emissions and by-products that may have environmental and health impacts. The specific emissions depend on the welding method used, materials welded, and operating conditions

## Slide 4: Key Green Welding Parameters
Inverter Technology
High-Frequency Start Systems
Advanced Welding Processes
Energy-Efficient Lighting
Energy Recovery Systems
Efficient Power Sources
Energy Consumption: Environmentally friendly welding aims to reduce the overall environmental impact, including energy consumption
Pulse Welding
Energy Management Practices
Welding Parameter Optimization
Automated Welding Systems

## Slide 5: Key Green Welding Parameters
Consumable Waste:
Minimize the generation of consumable waste such as welding electrodes, wires, and shielding gases
Material Usage and Waste: Minimizing material usage and waste
Base Metal Waste:
Manage and recycle metal scrap generated during welding to reduce overall material waste.

## Slide 6: Key Green Welding Parameters
Water Usage:
Evaluate the amount of water used in cooling systems and other aspects of the welding process
Regular Monitoring and Auditing
Weld Joint Design
Water Management Plans
Technology Upgrades
Cooling Systems
Water Recycling
Water-Efficient Cutting Methods
Low-Flow Water Cooling
Process Optimization
Use of Eco-Friendly Coolants
Rainwater Harvesting
Water Quality

## Slide 7: Key Green Welding Parameters
Environmental Compliance:
Ensure compliance with local, regional, and national environmental regulations related to welding activities
Regulatory Knowledge
Permitting and Reporting
Air Quality Compliance
Hazardous Material Management
Waste Management and Recycling
Water Quality Compliance
Record Keeping
Environmental Management Systems (EMS)
Community Engagement
Continuous Improvement

## Slide 8: Key Green Welding Parameters
Green Welding Technologies:
Αim to reduce the environmental impact of welding processes.
Friction Stir Welding
Electron Beam Welding
Pulsed Welding
Cold Metal Transfer
Plasma Arc Welding αnd Cutting
Advanced Welding Processes
High-Efficiency Power Sources
Efficient Cooling Systems
Robotics and Automation
Lightweight Materials and Thin-Section Welding
Energy Recovery Systems
Low-Emission Consumables
Welding Simulation Software
Green Coating Technologies
Carbon Footprint Analysis
Efficient Equipment

## Slide 9: Key Green Welding Parameters
Transportation Impact:
Τhe environmental impact of transporting materials, equipment, and finished products associated with welding activities.
Carbon Footprint:
Calculate and monitor the carbon footprint of welding activities, considering the overall greenhouse gas emissions associated with the process.
Environmental Management Systems (EMS):
Adopt an environmental management system to systematically manage and improve the environmental performance of welding operations.

## Slide 10: Measurement Types and Techniques for Green Welding
Emissions Monitoring: Air quality monitoring for particulate matter, metal fumes, and gases
Direct Sampling:
Collect air samples during welding activities and analyze them for pollutants
Continuous Emissions Monitoring Systems (CEMS): Install CEMS to continuously measure emissions during welding processes

## Slide 11: Measurement Types and Techniques for Green Welding
Real-Time Particle Counters
Particulate Matter (PM): Measure particle size and concentration
Personal Dust Monitors
Direct-Reading Dust Monitors
Gravimetric Samplers
High-Volume Air Samplers
Cascade Impactors
Indoor Air Quality (IAQ) Monitors
Nephelometers
Dust Trak Monitors

## Slide 12: Measurement Types and Techniques for Green Welding
Fume Composition: identification and quantification of specific metal fumes and gases
X-ray Fluorescence (XRF):
Gas Chromatography-Mass Spectrometry
X-ray Diffraction (XRD):
Inductively Coupled Plasma Mass Spectrometry (ICP-MS)

## Slide 13: Measurement Types and Techniques for Green Welding
Volatile Organic Compounds (VOCs): Detection and quantification of organic compounds
Photoionization Detector
Gas Chromatography-Mass Spectrometry
Gas Chromatography

## Slide 14: Measurement Types and Techniques for Green Welding
Gaseous Emissions: Monitoring of specific gases such as nitrogen oxides (NOx), sulfur dioxide (SO2), carbon monoxide (CO), and ozone (O3) , and other gases produced during the welding process
Gas Analyzers
Gas Chromatography (GC):
Infrared Gas Analyzers (IRGA):

## Slide 15: Measurement Types and Techniques for Green Welding
Gas Flow Rates Measuring gas flow rates (volume of gases) in welding processes is essential for ensuring the proper shielding of the weld area and achieving high-quality welds. The flow rates of shielding gases, such as argon, carbon dioxide, or a mixture of gases, are critical parameters that impact the stability of the arc, weld bead formation, and overall weld quality.
Flowmeters:
Rotameters:
Mass Flow Meters:

## Slide 16: Measurement Types and Techniques for Green Welding
Energy Consumption Measurement of energy usage during welding operations. We choose the method that best fits our specific needs and the type of welding process. Combining multiple measurement techniques may offer a more comprehensive understanding of energy consumption during welding
Utility Bills
Power Meters

## Slide 17: Measurement Types and Techniques for Green Welding
Material Efficiency: Measurement of material usage and waste generation, to optimize resources usage.
Weighing Scales
Waste Collection and Analysis
Welding Consumable Monitoring Devices
Cutting Pattern Optimization Software
Volume Measurement Devices

## Slide 18: Measurement Types and Techniques for Green Welding
Water Usage Measurement of water consumption in welding operations.
flow meters
data logging systems
Drip Pans and Collection Systems
Water Quality Sensors

## Slide 19: Measurement Types and Techniques for Green Welding
Greenhouse Gas Emissions Measurement of greenhouse gas emissions associated with welding processes.
Emission Factors
Waste Audits
Carbon Footprint Analysis:
Waste Generation and Recycling Measurement of waste generation and recycling rates.
Regular monitoring and measurement
Recycling Tracking

## Slide 20: International Standard, European Legislation and Acceptance criteria
International Standards
ISO 14001
REACH Regulation (EC) No 1907/2006
European Waste Framework Directive (2008/98/EC):
ISO 3834
European Legislation
RoHS Directive (2011/65/EU)
Specify the requirements for an environmental management system (EMS), for organizations to manage their environmental impact, including those related to welding processes
Quality requirements for fusion welding of metallic materials. While it primarily focuses on quality aspects, adherence to these standards can indirectly contribute to environmental considerations
Regulation that addresses the production and use of chemical substances. Compliance with REACH is essential for managing the environmental impact of welding consumables and chemicals used in the process.
The Restriction of Hazardous Substances (RoHS) Directive restricts the use of certain hazardous substances in electrical and electronic equipment. While not specific to welding, it may impact the selection of materials and components used in welding equipment.
Legal framework for waste management in the European Union. It emphasizes waste prevention and the promotion of recycling, which can be relevant for managing waste generated during welding processes.

## Slide 21: International Standard, European Legislation and Acceptance criteria
Acceptance Criteria:
Environmental Performance Indicators
Customer Requirements
Performance Benchmarking
Adherence to Industry Standards
Certification to Environmental Standards
Legal Compliance:
Companies may establish specific environmental performance indicators as acceptance criteria. These can include metrics related to energy efficiency, emissions reduction, and waste minimization in welding operations.
Industries may have specific standards or guidelines that set acceptance criteria for environmentally friendly welding practices. These could cover aspects such as emissions control, waste management, and energy efficiency.
Customers may specify environmental criteria in contracts or procurement agreements. Adherence to these criteria becomes a condition for acceptance.
Certification to recognized environmental standards, such as ISO 14001, may serve as acceptance criteria, demonstrating a commitment to environmental management in welding operations.
Organizations may establish acceptance criteria based on benchmarking against industry best practices.
Compliance with applicable environmental laws and regulations serves as a fundamental acceptance criteria.

## Slide 22: The influence of novel approaches on overall emission for environmentally friendly welding
Influence on Emissions of
Advanced Welding Processes
Electron Beam Welding (EBW)
Friction Stir Welding (FSW)
solid-state welding process that generates less hea, reduces the need for shielding gases and minimizes fume emissions
Operates in a vacuum, minimizing the need for shielding gases resulting in lower emissions
Influence on Emissions of
Pulsed Welding Technologies
Pulsed MIG/TIG Welding
Cold Metal Transfer (CMT)
Pulsed welding processes allow better control of heat input, resulting in reduced energy consumption and less spatter. This can contribute to lower emissions and improved efficiency.
CMT operates at lower temperatures, reducing heat input and minimizing emissions. It is particularly effective for welding thin sections and dissimilar materials

## Slide 23: The influence of novel approaches on overall emission for environmentally friendly welding
Inverter Technology
Inverter-based welding machines are more energy-efficient compared to traditional transformer-based machines. This can lead to overall energy savings and a reduction in emissions.
Influence on Emissions of
Efficient Power Sources
Influence on Emissions of
Low-Emission Consumables
Eco-Friendly Coatings
Low-Fume Welding Wires and Electrodes
Applying environmentally friendly coatings can reduce the need for pre-welding cleaning processes, decreasing the use of solvents and chemicals that contribute to emissions.
The use of low-fume welding consumables can help minimize airborne particulate matter and fumes, improving air quality and reducing overall emissions
Influence on Emissions of
Green Coating Technologies

## Slide 24: The influence of novel approaches on overall emission for environmentally friendly welding
Automated Welding Processes
Robotics and automation can optimize welding parameters, leading to more consistent and efficient processes. This can result in reduced energy consumption and emissions.
Influence on Emissions of
Robotics and Automation
Influence on Emissions of
Welding Simulation Software
Lightweight Materials and Thin-Section Welding
Virtual Testing and Optimization
Using lightweight materials and welding thin sections can reduce material consumption, energy requirements, and overall emissions.
Simulation software allows virtual testing and optimization of welding parameters, reducing the need for physical trial and error. This can lead to more efficient processes, minimizing emissions during experimentation
Influence on Emissions of
Material and Process Optimization:

## Slide 25: The influence of novel approaches on overall emission for environmentally friendly welding
Energy Recovery Systems
Some modern welding equipment includes energy recovery systems that capture and reuse energy, improving overall efficiency and reducing emissions
Influence on Emissions of
Energy Recovery Systems
Influence on Emissions of
Carbon Footprint Analysis and Management
Continuous Improvement Strategies:
Regularly conducting carbon footprint analyses and implementing continuous improvement strategies can identify opportunities to further reduce emissions throughout the welding process.

## Slide 26: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Generally produces lower emissions compared to some other processes.
Gas Metal Arc Welding (GMAW) / MIG Welding
Emissions
Weld Quality
High deposition rates, good quality welds.
Use of shielding gases and consumables can contribute to environmental impact
Sensitive to wind and atmospheric conditions.

## Slide 27: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Generally produces fewer emissions due to the use of inert shielding gases.
Gas Tungsten Arc Welding (GTAW) / TIG Welding
Emissions
Weld Quality
High-quality welds with precise control.
Tends to be a slower process compared to some others
Requires a high skill level, slower deposition rates

## Slide 28: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Simple process with minimal equipment, lower emissions
Shielded Metal Arc Welding (SMAW) / MMA Welding:
Emissions
Weld Quality
Versatile, suitable for outdoor and adverse conditions
Flux coating may contain certain elements impacting emissions
Slower compared to some other processes.

## Slide 29: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Can be designed as a low-emission process.
Flux-Cored Arc Welding (FCAW):
Emissions
Weld Quality
High deposition rates, suitable for thick materials.
Gas shielding or self-shielding options impact emissions.
May produce more spatter compared to other processes.

## Slide 30: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Can be a low-emission process when automated.
Submerged Arc Welding (SAW):
Emissions
Weld Quality
High deposition rates, efficient for thick sections
High heat input, potential for fume emissions.
Typically used in heavy fabrication.

## Slide 31: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Low emissions due to the solid-state nature of the process..
Friction Stir Welding (FSW):
Emissions
Weld Quality
Excellent for joining dissimilar materials, no melting.
Limited to certain materials and geometries.
Requires specialized equipment.

## Slide 32: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Minimal emissions as it operates in a vacuum.
Electron Beam Welding (EBW):
Emissions
Weld Quality
Precise and high-quality welds.
Requires high-vacuum conditions
Limited to specific applications.

## Slide 33: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Generally low emissions.
Plasma Arc Welding (PAW):
Emissions
Weld Quality
High energy concentration, good for precision welding.
Requires the use of plasma gas.
Similar to TIG but with higher energy.

## Slide 34: Performance of various welding techniques: emissions and welding quality evaluation for environmentally friendly welding
Low emissions as no consumables are used.
Resistance Spot Welding (RSW):
Emissions
Weld Quality
High-speed process, suitable for mass production..
Limited to specific applications..
Limited to certain material thicknesses.

## Slide 35: The Impact of various gases on emissions and welding quality for environmentally friendly welding
Argon is inert and does not react with the molten metal. It typically results in low emissions during welding
Argon (Ar):
Emissions Impact
Weld Quality
Provides a stable arc and good penetration. Often used for high-quality welds in applications such as stainless steel and aluminum
Argon is more commonly used in processes like TIG welding, which tend to have lower emissions compared to some other methods
Relatively more expensive than some other gases

## Slide 36: The Impact of various gases on emissions and welding quality for environmentally friendly welding
Helium can provide increased heat input and deeper penetration, but it can also increase emissions.
Helium (He):
Emissions Impact
Weld Quality
High thermal conductivity, suitable for deep-penetration welding.
Helium is often used in conjunction with other gases to balance performance and emissions.
Can result in a wider bead and increased spatter.

## Slide 37: The Impact of various gases on emissions and welding quality for environmentally friendly welding
CO2 is economical and widely used, but it can contribute to higher emissions.
Carbon Dioxide (CO2):
Emissions Impact
Weld Quality
Provides good penetration and is commonly used in GMAW (MIG) welding
May produce more fumes compared to inert gases.
Increased spatter and potential for porosity

## Slide 38: The Impact of various gases on emissions and welding quality for environmentally friendly welding
Oxygen is not commonly used as a shielding gas due to its oxidizing nature, which can lead to increased emissions.
Oxygen (O2):
Emissions Impact
Weld Quality
Can improve arc stability and reduce the risk of undercut
In certain processes, small amounts of oxygen may be added for specific benefits.
Oxygen is generally avoided in processes where oxide formation is a concern.

## Slide 39: The Impact of various gases on emissions and welding quality for environmentally friendly welding
Nitrogen is not commonly used as a primary shielding gas, but it may be present in the atmosphere and contribute to emissions.
Nitrogen (N2):
Emissions Impact
Weld Quality
Generally, not used as a primary shielding gas due to potential issues with arc stability and weld quality.
Nitrogen can react with molten metal, leading to nitride formation
May be used in some processes in small quantities for specific benefits.

## Slide 40: The impact of various gases and emissions on production time for environmentally friendly welding
Argon is inert and generally results in stable welding arcs with good penetration. This can contribute to efficient welding processes
Argon (Ar):
Impact on Production time
While argon is associated with stable welding, the choice of gas alone may not significantly impact production time
Choice of Shielding Gases

## Slide 41: The impact of various gases and emissions on production time for environmentally friendly welding
CO2 is often used in GMAW (MIG) welding due to its affordability and good penetration
Carbon Dioxide (CO2):
Impact on Production time
CO2 may contribute to increased spatter, which could require additional time for post-weld cleanup.
Choice of Shielding Gases

## Slide 42: The impact of various gases and emissions on production time for environmentally friendly welding
Helium can provide increased heat input and penetration, potentially reducing welding time for certain applications
Helium (He):
Impact on Production time
The cost of helium may be a consideration, and adjustments to welding parameters are needed for optimal results.
Choice of Shielding Gases

## Slide 43: The impact of various gases and emissions on production time for environmentally friendly welding
Gas mixtures are often used to balance performance and emissions. Optimal gas mixtures can contribute to efficient welding
Gas Mixtures (Ar/CO2, Ar/O2, etc.):
Impact on Production time
Fine-tuning gas mixtures may be required, impacting setup time
Choice of Shielding Gases

## Slide 44: The impact of various gases and emissions on production time for environmentally friendly welding
Choosing low-emission gases aligns with environmentally friendly practices but may not have a direct impact on production time.
Low-Emission Gases
Impact on Production time
The environmental benefits may justify any potential minor adjustments in welding parameters
Emissions and Environmental Considerations

## Slide 45: The impact of various gases and emissions on production time for environmentally friendly welding
Regular emission monitoring ensures compliance with environmental standards and regulations.
Emission Monitoring and Compliance
Impact on Production time
Periodic monitoring may have a minimal impact on production time, but it is a necessary aspect of environmentally friendly practices.
Emissions and Environmental Considerations

## Slide 46: The impact of various gases and emissions on production time for environmentally friendly welding
Implementing efficient welding practices, such as using advanced welding processes or automation, can reduce production time.
Efficiency Improvements:
Impact on Production time
Initial setup and training may be required for the adoption of new technologies, impacting production initially.
Efficiency and Process Optimization

## Slide 47: The impact of various gases and emissions on production time for environmentally friendly welding
Optimizing welding parameters to reduce emissions can contribute to environmentally friendly welding
Process Optimization for Emission Reduction:
Impact on Production time
Fine-tuning parameters may be necessary, potentially affecting initial setup time..
Efficiency and Process Optimization

## Slide 48: GREENWELDING examples
Renewable energy application in welding procedures
A company occupied with welding procedures in South Italy decides to shift to renewable energy for it welding procedures
The company installs solar panels on its facilities’ roof to generate electricity. They invest in energy-efficient welding power sources and LED lighting. Transition to solar power significantly reduces their dependence on the grid and lowers overall carbon emissions.
A construction company aims to reduce its environmental impact by using in welding consumables made by recycled materials.
Welding consumables made by recycled materials
The company asks a suppliers to produce welding wires and electrodes made from recycled materials. They are conducting weldability tests to ensure the recycled consumables are conform with the required quality standards. If yes, by this way the construction company not only reduces its demand for new raw material but also lowers the total carbon footprint during the welding process.

## Slide 49: GREENWELDING examples
Welding Fume emissions
A large-scale manufacturing company understands the importance of controlling the emission of welding fumes for both welders health and environmental considerations.
The company invests in advanced fume extraction and filtration systems in its welding workshop facilities. High-efficiency filters are used to commit and filter welding fumes before releasing them to the atmosphere. By this way they reduce the air pollution and provides a healthier working environment.
Welding Robot Integration for Precision and Efficiency
An automotive assembly plant wants to improve the precision and efficiency of their welding operations..
The company invests in robotic welding systems that offer high precision and efficiency. These robots use advanced sensors to optimize welding parameters, minimizing the need for rework. The automation not only increase product quality but also reduces energy consumption compared to traditional manual welding processes.

## Slide 50: GREENWELDING examples
A shipbuilding company aims to reduce waste and energy consumption in their welding operations..
Lean Manufacturing and Efficient Welding Processes
The company adopts lean manufacturing principles to optimize their welding processes. They streamline workflows, reduce idle time, and implement efficient welding techniques. As a result, they achieve higher productivity with less energy consumption and waste generation. This approach not only benefits the environment but also improves the company's bottom line.
Lean manufacturing is a methodology that focuses on minimizing waste within manufacturing systems while simultaneously maximizing productivity. Waste is anything that customers do not believe adds value and are not willing to pay for.

## Slide 51: Any questions?
Thank you!